## Slide 1
Reservoirs in LISFLOOD
Jesús Casado Rodríguez
JRC-E1
Data
Reservoir simulation
2.1 Current routine
2.2 Other approaches

## Slide 2
1. Data
Reservoir attributes
EFAS5 includes 1423 reservoirs (121 in Norway)
Very few reservoirs from GRanD are missing
D2 will get the ICOLD data set

## Slide 3
1. Data
Reservoir time series
Required to improve the reservoir routine
ResOpsUS:
  679 major reservoirs in the US
  Daily time series: inflow, storage, outflow, evaporation
Anuario de Aforos de España:
    394 reservoirs in Spain
    Daily time series: storage, outflow
EFAS Hydrological Data Collection Centre: Sava
D2 has contacted possible colaborators
Is the data in Norway available?

## Slide 4
Qc
Qn’
Vc
Vn
Vn’
Vf
Qf
outflow
storage
inflow
Different from Burek 2013
Parameters:
  3 default (storage)
  2 reservoir-specific (outflow)
  2 calibrated
No seasonality
No reservoir use
2. Reservoir simulation
Current routine
κ=1.2
1

## Slide 5
2. Reservoir simulation
Comparison of the simulated and observed time series for 121 reservoirs
The performance in terms of outflow is fairly good given the errors imposed by the inflow
The main issue is the performance in terms of storage
Current routine
: GloFAS4 performance
github.com/casadoj/LF_water_bodies/docs/performance_US.md

## Slide 6
k = 1.2?
no flood
regulation
Q
t
inflow
outflow
2. Reservoir simulation
Current routine
non-calibrated
tendency to fill up
Q
S
I
: the example of the Boysen Reservoir (Mississippi)
github.com/casadoj/LF_water_bodies/docs/performance_US.md

## Slide 7
Qc
Qn
Vc
Vn
Vn’
Vf
Qf
outflow
storage
inflow
2. Reservoir simulation
κ
1
93 reservoirs from ResOpsUS
Optimization algorithm: SCE-UA
Objective function: KGE’
Target variable:
  Outflow
  Storage
  Outflow & storage
Current routine
: calibration
github.com/casadoj/LF_water_bodies/docs/calibration_US.md

## Slide 8
2. Reservoir simulation
Calibrating only storage gives surprisingly good results → global storage data sets from satellite data: GRSAD, ReaLSAT, ReGeom, DAHITI, Res-CN
Current routine
: calibration
github.com/casadoj/LF_water_bodies/docs/calibration_US.md

## Slide 9
2. Reservoir simulation
no flood
regulation
tendency to fill up
no κ
Current routine
: calibration of the Boysen Reservoir (Mississippi)
Q
S
I
github.com/casadoj/LF_water_bodies/docs/calibration_US.md

## Slide 10
0.5·Qn
Qn
0.5·Vf
Vf
Ve
Qf
outflow
storage
inflow
2. Reservoir simulation
Other approaches:
κ
1
inflow < Qf
inflow ≥ Qf
Evolution from Burek 2013
All parameters are reservoir-specific
No seasonality
No reservoir use
Hanazaki et al. (2022)

## Slide 11
2. Reservoir simulation
Q
S
I
Other approaches: Hanazaki et al. (2022)

## Slide 12
2. Reservoir simulation
Other approaches:
adding seasonality, Turner et al. (2021)

## Slide 13
2. Reservoir simulation
Extend to multiple reservoirs to create a general model
Add static parameters: reservoir use, coordinates, climate, reservoir/dam properties, month, day of the week…
Other approaches:
deep learning, Ramos-Oliveira et al. (2023)

## Slide 14
Thank you
github.com/casadoj/LF_water_bodies