## Slide 1: Reservoirs, lakes, and wetlands
Add lakes and reservoirs
Improve the reservoir simulation
Add wetlands in the model simulation

## Slide 2: Reservoirs, lakes, and wetlands
Comparison of the simulated and observed time series for 121 reservoirs.
The performance in terms of outflow is fairly good given the errors imposed by the inflow
The main issue is the performance in terms of storage
Recap: GloFASv4 performance
github.com/casadoj/LF_water_bodies/docs/performance_US.md

## Slide 3: Reservoirs, lakes, and wetlands
Qc
Qn
Vc
Vn
Vn’
Vf
Qf
outflow
storage
inflow
κ
1
93 reservoirs from ResOpsUS
Optimization algorithm: SCE-UA
Objective function: KGE’
Target variable:
  Outflow
  Storage
  Outflow & storage
github.com/casadoj/LF_water_bodies/docs/calibration_US.md
Calibration of the current routine

## Slide 4: Reservoirs, lakes, and wetlands
Calibrating only storage gives surprisingly good results → global storage data sets from satellite data: GRSAD, ReaLSAT, ReGeom, DAHITI, Res-CN
Calibration of the current routine
github.com/casadoj/LF_water_bodies/docs/calibration_US.md

## Slide 5: Reservoirs, lakes, and wetlands
0.5·Qn
Qn
0.5·Vf
Vf
Ve
Qf
outflow
storage
inflow
κ
1
inflow < Qf
inflow ≥ Qf
Evolution from Burek et al. (2013)
All parameters are reservoir-specific
No seasonality
No reservoir use
Approach by Hanazaki et al. (2022)

## Slide 6: Reservoirs, lakes, and wetlands
Performance:
  Similar in terms of outflow
  Higher in terms of storage
Less realistic hydrographs → need for other metric?
Approach by Hanazaki et al. (2022)

## Slide 7: Reservoirs, lakes, and wetlands
Estimate parameters based on observed data
  Bivariable calibration: storage & outflow
  Regionalization of parameters based on reservoir use
Test the evolution of Burek 2013 by Hanazaki et al. (2022)
Test the approach to seasonality by Turner et al. (2021)
Deep learning? Ramos-Oliveira et al. (2023), Liu et al. (2019) → SEED-FD
Following steps